## Slide 1: Embedded C
Trainer:
Bhumika Narang
C-DAC

## Slide 2: typedef in C:
typedef is a keyword in C used to create aliases for existing data types. It simplifies the code, improves readability, and can make maintenance easier by allowing you to use more descriptive names for data types.
Improved Readability: Provides more meaningful names for types, making code easier to understand.
Ease of Maintenance: Changes to the underlying type can be managed in one place by updating the typedef, without modifying all occurrences in the code.
Simplifies Complex Declarations: Makes complex type declarations easier to manage and understand, especially for pointers and function pointers.
Basic Syntax:
typedef existing_type new_type_name;
• existing_type: The existing type you want to create an alias for.
• new_type_name: The new name you want to use for the existing type.

## Slide 3: Basic typedef:
#include <stdio.h>
typedef unsigned long ulong;
int main() {
ulong num = 1000000;
printf("Number: %lu\n", num); // Output: Number: 1000000
return 0;
}
Here, ulong is now an alias for unsigned long.

## Slide 4: typedef for Structs:
#include <stdio.h>
typedef struct {
int x;
int y;
} Point;
int main() {
Point p1;
p1.x = 10;
p1.y = 20;
printf("Point coordinates: (%d, %d)\n", p1.x, p1.y); // Output: Point coordinates: (10, 20)
return 0;
}
//Here, Point is an alias for the struct type, making it easier to declare variables of this type.

## Slide 5: typedef for Pointers:
#include <stdio.h>
typedef int* IntPtr;
int main() {
IntPtr ptr;
int value = 5;
ptr = &value;
printf("Value: %d\n", *ptr); // Output: Value: 5
return 0;
}
//here, IntPtr is an alias for int*, simplifying pointer declarations.

## Slide 6: typedef for Function Pointers:
#include <stdio.h>
typedef int (*FuncPtr)(int, int);
int add(int a, int b) {
return a + b;
}
int main() {
FuncPtr ptr = add;
printf("Sum: %d\n", ptr(5, 3)); // Output: Sum: 8
return 0;
}
//Here, FuncPtr is an alias for a pointer to a function that takes two int arguments and returns an int.

## Slide 7: typedef for Arrays:
#include <stdio.h>
typedef int IntArray[5];
int main() {
IntArray arr = {1, 2, 3, 4, 5};
for (int i = 0; i < 5; i++) {
printf("%d ", arr[i]);
}
printf("\n");
return 0;
}
//here, IntArray is an alias for an array of 5 int elements.

## Slide 8: typedef with Enum:
#include <stdio.h>
typedef enum {
RED,
GREEN,
BLUE
} Color;
int main() {
Color myColor = GREEN;
switch (myColor) {
case RED:
printf("Red\n");
break;
case GREEN:
printf("Green\n");
break;
case BLUE:
printf("Blue\n");
break;
default:
printf("Unknown color\n");
}
return 0;
}
Here, color is an alias for the enum type, simplifying the declaration and usage of enumerated values.

## Slide 9: Bit field operators in C:
Bit fields in C are used to allocate a specific number of bits for a variable.
It’s useful when you want to pack multiple variables into a smaller amount of memory or represent hardware registers and flags efficiently.
Bit fields are defined within a struct in C, specifying the number of bits each member should occupy.
Syntax:
struct StructName {
type memberName : numberOfBits;
};
type: Typically an integer type (int, unsigned int, etc.).
memberName: The name of the bit field member.
numberOfBits: The number of bits allocated to this member.

## Slide 10: Example:
#include <stdio.h>
struct {
unsigned int a : 1;
unsigned int b : 3;
unsigned int c : 4;
} bitField;
int main() {
bitField.a = 1; // 1 bit, range: 0-1
bitField.b = 5; // 3 bits, range: 0-7
bitField.c = 10; // 4 bits, range: 0-15
printf("a: %d\n", bitField.a);
printf("b: %d\n", bitField.b);
printf("c: %d\n", bitField.c);
return 0;
}

## Slide 11: Bit Field Access and Usage: Accessing and manipulating bit fields is similar to regular struct members, but with the bit size constraints.
#include <stdio.h>
struct {
unsigned int flag1 : 1;
unsigned int flag2 : 1;
unsigned int value : 6;
} status;
int main() {
status.flag1 = 1; // Set flag1
status.flag2 = 0; // Clear flag2
status.value = 45; // Set value (6 bits, range: 0-63)
printf("flag1: %d\n", status.flag1);
printf("flag2: %d\n", status.flag2);
printf("value: %d\n", status.value);
return 0;
}

## Slide 12
Advantages of Bit Fields:
1. Memory Efficiency: Bit fields allow you to use memory more efficiently by allocating only as many bits as necessary for each field.
2. Hardware Representation: Useful for representing hardware registers and communication protocols, where each bit or group of bits has a specific meaning.
3. Improved Readability: Provides a clear and structured way to represent flags and bit-based values.
Limitations of Bit Fields
1. Portability Issues: Bit field behavior can be implementation-specific, leading to portability issues between different compilers or architectures.
2. Limited Data Types: Only integer types (int, unsigned int, etc.) are allowed for bit fields.
3. Alignment and Padding: Compilers may add padding bits for alignment purposes, which can affect the actual memory layout.

## Slide 13: Bitwise Operators: Bitwise operators are often used with bit fields for setting, clearing, and toggling specific bits.
Operation(Operator) | Task
AND (&) | Clears specific bits
OR (¦) | Sets specific bits
XOR (^) | Toggles specific bits
NOT (~) | Inverts all bits
Shift Left (<<) | Shifts bits to the left
Shift Right (>>) | Shifts bits to the right

## Slide 14: Bit operations in C: Bit operations in C are fundamental for manipulating individual bits within data. These operations are essential in low-level programming, embedded systems, and performance-critical applications. They are used for tasks such as setting, clearing, and toggling specific bits, as well as performing bitwise calculations.
Bitwise AND (&)
Bitwise OR (|)
Bitwise XOR (^)
Bitwise NOT (~)
Left Shift (<<)
Right Shift (>>)

## Slide 15: Bitwise AND (&): Performs a logical AND on each pair of corresponding bits of two operands.
unsigned int a = 0xF0F0; // 1111 0000 1111 0000 in binary
unsigned int b = 0x0F0F; // 0000 1111 0000 1111 in binary
unsigned int result = a & b; // 0000 0000 0000 0000 in binary
printf("Result of AND: 0x%X\n", result); // Output: 0x0

## Slide 16: Bitwise OR (|): Performs a logical OR on each pair of corresponding bits of two operands.
unsigned int a = 0xF0F0; // 1111 0000 1111 0000 in binary
unsigned int b = 0x0F0F; // 0000 1111 0000 1111 in binary
unsigned int result = a | b; // 1111 1111 1111 1111 in binary
printf("Result of OR: 0x%X\n", result); // Output: 0xFFFF

## Slide 17: Bitwise XOR (^): Performs a logical XOR (exclusive OR) on each pair of corresponding bits of two operands.
unsigned int a = 0xF0F0; // 1111 0000 1111 0000 in binary
unsigned int b = 0x0F0F; // 0000 1111 0000 1111 in binary
unsigned int result = a ^ b; // 1111 1111 1111 1111 in binary
printf("Result of XOR: 0x%X\n", result); // Output: 0xFFFF

## Slide 18: Bitwise NOT (~): Flips all the bits of the operand.
unsigned int a = 0xF0F0; // 1111 0000 1111 0000 in binary
unsigned int result = ~a; // 0000 1111 0000 1111 in binary
printf("Result of NOT: 0x%X\n", result); // Output: 0x0F0F

## Slide 19: Left Shift (<<): Shifts the bits of the operand to the left by a specified number of positions, filling the vacated bits with zeros.
unsigned int a = 0x0F; // 0000 1111 in binary
unsigned int result = a << 2; // 0011 1100 in binary
printf("Result of Left Shift: 0x%X\n", result); // Output: 0x3C

## Slide 20: Right Shift (>>): Shifts the bits of the operand to the right by a specified number of positions. For unsigned integers, the vacated bits are filled with zeros. For signed integers, the behaviour can be implementation-defined (usually arithmetic shift).
unsigned int a = 0x0F; // 0000 1111 in binary
unsigned int result = a >> 2; // 0000 0011 in binary
printf("Result of Right Shift: 0x%X\n", result); // Output: 0x03

## Slide 21: Bit Manipulation Techniques:
1. Setting a Bit:
o Description: Set a specific bit to 1.
unsigned int value = 0x0F; // 0000 1111 in binary
unsigned int bit_position = 5; // Bit to set (0-indexed)
value |= (1 << bit_position); // Set the 5th bit
printf("After setting bit: 0x%X\n", value); // Output: 0x3F
2. Clearing a Bit:
o Description: Set a specific bit to 0.
unsigned int value = 0x3F; // 0011 1111 in binary
unsigned int bit_position = 5; // Bit to clear (0-indexed)
value &= ~(1 << bit_position); // Clear the 5th bit
printf("After clearing bit: 0x%X\n", value); // Output: 0x1F

## Slide 22
3. Toggling a Bit:
o Description: Flip the value of a specific bit.
unsigned int value = 0x1F; // 0001 1111 in binary
unsigned int bit_position = 4; // Bit to toggle (0-indexed)
value ^= (1 << bit_position); // Toggle the 4th bit
printf("After toggling bit: 0x%X\n", value); // Output: 0x1F
4. Checking a Bit:
o Description: Check if a specific bit is set.
unsigned int value = 0x3F; // 0011 1111 in binary
unsigned int bit_position = 5; // Bit to check (0-indexed)
if (value & (1 << bit_position)) {
printf("Bit %d is set\n", bit_position);
} else {
printf("Bit %d is not set\n", bit_position);
}

## Slide 23
5. Extracting a Bit Field:
o Description: Extract a field of bits from a number.
unsigned int value = 0xFF; // 1111 1111 in binary
unsigned int start = 4; // Start position of the bit field
unsigned int length = 4; // Length of the bit field
unsigned int mask = ((1 << length) - 1) << start;
unsigned int field = (value & mask) >> start;
printf("Extracted field: 0x%X\n", field); // Output: 0xF
#define LED_PIN 0x01 // Bit 0
#define BUTTON_PIN 0x02 // Bit 1
void configure_pins(unsigned int *register) {
*register |= LED_PIN; // Set LED_PIN bit
*register &= ~BUTTON_PIN; // Clear BUTTON_PIN bit
}
Embedded System Example

## Slide 24: Example:
#include <stdio.h>
int main() {
unsigned char flags = 0b10101010; // Binary representation: 10101010
// Set the 2nd bit (0-based index)
flags |= (1 << 2); // Binary: 10101110
// Clear the 4th bit
flags &= ~(1 << 4); // Binary: 10100110
// Toggle the 6th bit
flags ^= (1 << 6); // Binary: 11100110
printf("Flags: 0x%X\n", flags); // Output: Flags: 0xEE
return 0;
}

## Slide 25: Pointers with structures
Pointers to structures in C are used extensively in various applications, including dynamic memory allocation, linked lists, trees, and other complex data structures. Defining and Using Pointers to Structures
Defining a Structure
#include <stdio.h>
struct Point {
int x;
int y;
};

## Slide 26: Declaring and Initializing a Pointer to a Structure:
#include <stdio.h>
struct Point {
int x;
int y;
};
int main() {
struct Point p = {10, 20};
struct Point *pPtr = &p; // pPtr is a pointer to struct Point
// Accessing members using the pointer
printf("x: %d, y: %d\n", pPtr->x, pPtr->y); // Output: x: 10, y: 20
return 0;
}
• struct Point *pPtr = &p; declares a pointer to a structure and initializes it with the address of p.
• pPtr->x and pPtr->y are used to access the members of the structure via the pointer.

## Slide 27: Dynamic Memory Allocation with Structures (Allocating Memory Dynamically):
#include <stdio.h>
#include <stdlib.h>
struct Point {
int x;
int y;
};
int main() {
// Allocate memory for a struct Point
struct Point *pPtr = (struct Point *)malloc(sizeof(struct Point));
if (pPtr == NULL) {
printf("Memory allocation failed\n");
return 1;
}
// Initialize members
pPtr->x = 30;
pPtr->y = 40;
// Access members
printf("x: %d, y: %d\n", pPtr->x, pPtr->y); // Output: x: 30, y: 40
// Free allocated memory
free(pPtr);
return 0;
}
• malloc allocates memory for a struct Point, and pPtr is a pointer to this dynamically allocated memory.
• Always check if malloc returns NULL to ensure memory allocation was successful.
• Remember to free the allocated memory to avoid memory leaks.

## Slide 28: Arrays of Structures and Pointers:
#include <stdio.h>
struct Point {
int x;
int y;
};
int main() {
struct Point points[3] = {{1, 2}, {3, 4}, {5, 6}};
struct Point *pPtr = points; // pPtr points to the first element of the array
for (int i = 0; i < 3; i++) {
printf("Point %d -> x: %d, y: %d\n", i, (pPtr + i)->x, (pPtr + i)->y);
}
return 0;
}
• pPtr points to the first element of the points array.
• (pPtr + i)->x and (pPtr + i)->y are used to access members of each structure in the array.

## Slide 29: Linked Lists with Structures and Pointers:
#include <stdio.h>
#include <stdlib.h>
struct Node {
int data;
struct Node *next;
};
int main() {
// Creating nodes
struct Node *head = (struct Node *)malloc(sizeof(struct Node));
struct Node *second = (struct Node *)malloc(sizeof(struct Node));
struct Node *third = (struct Node *)malloc(sizeof(struct Node));
// Initialize nodes
head->data = 1;
head->next = second;
second->data = 2;
second->next = third;
third->data = 3;
third->next = NULL;
struct Node *temp = head; // Traversing the list
while (temp != NULL) {
printf("Data: %d\n", temp->data); // Output: Data: 1, Data: 2, Data: 3
temp = temp->next;
}
free(third); // Free allocated memory
free(second);
free(head);
return 0;
}

## Slide 30: Pre-processors in C
Pre-processors in C are tools that operate on the source code before the actual compilation process begins.
Pre-processors play a crucial role in making C programs more flexible and manageable by allowing conditional compilation and code abstraction through macros.
They handle directives that control the compilation process, allowing for
          Macro Definition(#define)
          File Inclusion(#include)
          Conditional Compilation(#if, #ifdef, #ifndef, #else, #elif, #endif)
          Macro Undefinition (#undef)
          Pragma Directive (#pragma)

## Slide 31: Macro Definition (#define): Macros are used to define constant values or functions that are substituted in the code.
#define PI 3.14
#define CIRCLE_AREA(radius) (PI * (radius) * (radius))
int main() {
double radius = 5.0;
double area = CIRCLE_AREA(radius);
printf("Area of circle: %f\n", area); // Output: Area of circle: 78.50
return 0;
}

## Slide 32: Example of Macro Definition :
o Object-like Macros: Replace identifiers with code fragments.
#define MAX 100
int array[MAX]; // Expands to int array[100];
o Function-like Macros: Perform parameterized substitution.
#define SQUARE(x) ((x) * (x))
int y = SQUARE(5); // Expands to int y = ((5) * (5));

## Slide 33: File Inclusion (#include) This directive is used to include the contents of another file.
#include <stdio.h> // Standard library header file
#include "myheader.h" // User-defined header file
int main() {
printf("Hello, World!\n");
return 0;
}
o Standard Library Files: Use angle brackets < >.
#include <stdio.h>
o User-defined Files: Use double quotes " ".
#include "myheader.h"

## Slide 34: Conditional Compilation (#if, #ifdef, #ifndef, #else, #elif, #endif) Conditional compilation allows compiling code selectively based on certain conditions.
#define DEBUG
int main() {
#ifdef DEBUG
printf("Debug mode is ON\n");
#else
printf("Debug mode is OFF\n");
#endif
return 0;
}

## Slide 35: Conditional Compilation Example:
o Conditional Code Inclusion:
#if EXPRESSION
// Code to include if EXPRESSION is true
#endif
o Check if Macro is Defined:
#ifdef MACRO
// Code to include if MACRO is defined
#endif
o Check if Macro is Not Defined:
#ifndef MACRO
// Code to include if MACRO is not defined
#endif
o Alternative Conditions:
#if EXPRESSION
// Code if EXPRESSION is true
#elif ANOTHER_EXPRESSION
// Code if ANOTHER_EXPRESSION is true
#else
// Code if none of the above expressions are true
#endif

## Slide 36: Macro Undefinition (#undef) This directive is used to undefine a macro.
#define TEMP 100
#undef TEMP
#define TEMP 200
int main() {
printf("TEMP: %d\n", TEMP); // Output: TEMP: 200
return 0;
}
Remove Macro Definition:
#define BUFFER_SIZE 1024
#undef BUFFER_SIZE
#define BUFFER_SIZE 2048

## Slide 37: Pragma Directive (#pragma): The #pragma directive is used to provide additional information to the compiler.
#pragma message("Compiling this code")
int main() {
printf("Pragma directive demo\n");
return 0;
}
Compiler-specific Instructions:
#pragma warning(disable: 4996) // Disable a specific warning in MSVC

## Slide 38: Example of a Combined Use of Pre-processor Directives:
#include <stdio.h>
#define PI 3.14159
#define AREA(radius) (PI * (radius) * (radius))
#define DEBUG
int main() {
double r = 5.0;
double area = AREA(r);
printf("Area of circle: %f\n", area);
#ifdef DEBUG
printf("Debug mode: Radius = %f, Area = %f\n", r, area);
#endif
return 0;
}

## Slide 39: Interfacing C with Assembly Language: Interfacing C with Assembly language can be crucial for embedded systems and performance-critical applications. It allows developers to optimize specific parts of the code for speed or size, and to interact directly with hardware.
Advantages:
Performance Optimization: Assembly code can be written for performance-critical sections to optimize speed.
Hardware Access: Direct interaction with hardware components that require precise control not possible with high-level languages.
Legacy Code Integration: Incorporating existing assembly routines into new C codebases.
Methods to Interface C with Assembly:
Inline Assembly
Separate Assembly Files
Compiler Intrinsic

## Slide 40: Inline Assembly: Inline assembly allows embedding assembly instructions directly within C code using compiler-specific syntax. This method is compiler-dependent.
#include <stdio.h>
int main() {
int result;
asm("movl $5, %%eax;"
"movl $3, %%ebx;"
"addl %%ebx, %%eax;"
"movl %%eax, %0;"
: "=r" (result) // Output operand
: // Input operands (none)
: "%eax", "%ebx" // Clobbered registers
);
printf("Result: %d\n", result); // Output: Result: 8
return 0;
}

## Slide 41: Separate Assembly Files: Assembly code is written in separate files, assembled with an assembler, and linked with C code. This method is more portable across different compilers.
Assembly File (add.asm):
section .text
global add_numbers
add_numbers:
mov eax, [esp+4] ; Get the first argument
mov ebx, [esp+8] ; Get the second argument
add eax, ebx ; Add them
ret
C File(main.c):
#include <stdio.h>
extern int add_numbers(int a, int b);
int main() {
int result = add_numbers(5, 3);
printf("Result: %d\n", result); // Output: Result: 8
return 0;
}

## Slide 42: Compiler Intrinsic: For some operations, compilers provide intrinsic, which are built-in functions that generate specific assembly instructions.
#include <stdio.h>
#include <x86intrin.h> // Header for GCC intrinsics
int main() {
int a = 5, b = 3;
int result = _addcarry_u32(0, a, b, &result); // Adds a and b with carry-in
printf("Result: %d\n", result); // Output: Result: 8
return 0;
}

## Slide 43: Files Input/Output in C:
File Input/Output (I/O) in C is managed through a set of standard library functions that allow for reading from and writing to files.
The C Standard Library provides a robust set of functions for file handling, which are part of the stdio.h header.
File Modes:
• "r": Read-only mode. The file must exist.
• "w": Write-only mode. Creates a new file or truncates an existing file.
• "a": Append mode. Adds data to the end of the file.
• "r+": Read and write mode. The file must exist.
• "w+": Read and write mode. Creates a new file or truncates an existing file.
• "a+": Read and write mode. Appends data to the end of the file and creates the file if it does not exist.

## Slide 44: Opening a File: To perform file operations, you first need to open a file using fopen(). This function returns a file pointer of type FILE*.
Syntax:
FILE *fopen(const char *filename, const char *mode);
o filename: The name of the file to open.
o mode: The file access mode (e.g., "r" for read, "w" for write, "a" for append).
Example:
FILE *file = fopen("example.txt", "r"); // Open file for reading
if (file == NULL) {
perror("Error opening file");
return 1;
}

## Slide 45: Reading from a File: Use functions like fgetc(), fgets(), and fread() to read data from a file.
char buffer[100];
// Read a single character
int ch = fgetc(file);
if (ch != EOF) {
printf("Character read: %c\n", ch);
}
// Read a line of text
if (fgets(buffer, sizeof(buffer), file) != NULL) {
printf("Line read: %s", buffer);
}
// Read binary data
size_t bytesRead = fread(buffer, 1, sizeof(buffer), file);
printf("Bytes read: %zu\n", bytesRead);

## Slide 46: Writing to a File: Use functions like fputc(), fputs(), and fwrite() to write data to a file.
// Write a single character
fputc('A', file);
// Write a string
fputs("Hello, World!\n", file);
// Write binary data
const char data[] = "Binary data";
fwrite(data, sizeof(char), sizeof(data), file);

## Slide 47: Closing a File: Always close a file when you're done with it using fclose(). This ensures that all data is properly written and resources are released.
Syntax:
int fclose(FILE *stream);
Example:
if (fclose(file) != 0) {
perror("Error closing file");
}

## Slide 48: Error Handling: Use ferror() and clearerr() to handle and clear file errors.
Example:
if (ferror(file)) {
perror("File error");
clearerr(file); // Clear error indicators
}

## Slide 49
#include <stdio.h>
int main() {
// Open file for writing
FILE *file = fopen("example.txt", "w");
if (file == NULL) {
perror("Error opening file");
return 1;
}
// Write to the file
fprintf(file, "Hello, File I/O in C!\n");
// Close the file
if (fclose(file) != 0) {
perror("Error closing file");
return 1;
}
// Open file for reading
file = fopen("example.txt", "r");
if (file == NULL) {
perror("Error opening file");
return 1;
}
// Read from the file
char buffer[100];
if (fgets(buffer, sizeof(buffer), file) != NULL) {
printf("Read from file: %s", buffer);
}
// Close the file
if (fclose(file) != 0) {
perror("Error closing file");
return 1;
}
return 0; }

## Slide 50: Thank You